Technical Specifications Item/System/Equipment/Machinery are as under:

i) Thin Clients with Accessories: Quantity - 500 Nos.

| Parameters (1) | Specification (2) | A/D/N/C (3) |
| --- | --- | --- |
| Flash Memory | 8 GB capacity flash memory storage on internal Super Speed USB 3.0 modules |  |
| Main Memory | Integrated 2 GB DDR3L SDRAM system memory, 64 MB reserved for Graphics |  |
| Chasis | Fanless Chasis |  |
| Processor | Intel/AMD GX-209JA System-on-Chip (SOC), including a 1.0 GHz dual core APU and discrete-level GPUGhz Dual Core Processor or higher |  |
| BIOS | BIOS should be of the same OEM |  |
| Peripherals | (a) USB Optical mouse (b) 104 Keys USB OEM Keyboard |  |
| Network Interface | 10/100 / 1000 Mbps Ethernet (auto sensing) NIC, RJ45 connector. |  |
| Graphics | AMD/Intel Integrated Graphics or higher |  |
| Ports/Slots | 4 External USB 2.0 or higher |  |
|  | 1/8 inch 16 bit, stereo audio output, 8 bit mini mic input with internal speaker 1 VGA &1 DVI-D Port |  |
| (1) | (2) | (3) |
| Security | Option to enable/disable external USB Ports. |  |
| Display | Max Resolution 1920 x 1200 @ 60 Hz, 24 bpp |  |
| OS Support | Two operating systems in one. Enjoy the flexibility to choose between a locked-down and simple environment |  |
| OS Security Feature | With SMART Zero Core, or the more robust desktop-style interface. |  |
| Emulation/Protocol support | Citrix Receiver13.1 & HDX Support, xRDP with RemoteFX, Mozilla Firefox 31 Horizon View 3.2 Broker support Remote Management Agent Built in tool to capture TC image and redeploy using a USB pendrive. Terminal Emulation Suit. |  |
| Network | (a) TCP/IP with DNS and DHCP wake on LAN (b) DHCP support for automatic firmware upgrades & unit configuration. (c) PPPTP, L2TP, SNTP) |  |
| Manageability | OEM Management software to manage Thin Clients from Centralized Server: -Asset Track -Grouping Of Terminals -Device Online/Offline status -Configure Device Settings -Should support upgrade of group of thin client from central location -Power management: Reboot, shutdown, Wake-on-LAN |  |
| Power supply | 100-240 Volts AC, at 50-60 HZ, energy-saving automatic power-down, surge-tolerant, Must be external adapter to avoid internal heating |  |
| Regulatory Standards | Ergonomics- Approved ; Safety -UL 1950, CSA 950; TÜV-GS (EN60 950) ; - FCC Class B; CE Mark; EN55022B; VCCI, Energy Star. EPEAT Gold registered. |  |
| Warranty and Services | 5 Yrs. Comprehensive Warranty from OEM. Bidder/OEM Should have 150+ service centers across India (in Class- A, B, C Cities) exclusively there shall be service center in Hyderabad. Bidder/OEM should have 1 LS, 2LS,3LS backend infra for after sales support. Bidder/OEM Should have next Business Day response. Bidder/OEM Should have trained and certified Support staff. Bidder / OEM should have 6 days after sales support, i.e. Monday to Saturday. However for the USB Barcode reader, the warranty should be for 3 years. |  |
| Monitor | 18.5" LED Monitor from the same manufacturer. |  |
| USB Barcode Reader | One dimensional 14 characters Barcode reader compatible with the above thin client machine. |  |
| Certification | EPEAT Gold certified. |  |

ii)  High End Server

- Category-1: Quantity- 03 Nos.

| Parameters (1) | Specification (2) | A/D/N/C (3) |
| --- | --- | --- |
| Item | Description of Requirement for 4 CPU Servers populated with 2 Processors |  |
| Processor | The server should be supplied with two numbers of Intel® Xeon® E7-4830v4 (2.0GHz/14-core/35MB/115W) Processor Kit |  |
| Cache | 35 MB L3 cache memory |  |
| Chipset | Intel® C602J Chipset |  |
| Memory | 256 GB with DDR4 DIMMs and server should support upto 6TB memory supporting across 96 DIMM slots |  |
| Memory Features | Should support advanced memory features 1) Memory quarantine 2) Double data device correction 3) Single data device correction 4) Online Memory sparing 5) Memory mirroring |  |
| Integrated network controller | 1. 1Gb 4-port network adaptor supporting advanced features such as Large Send offload capability, TCP checksum and segmentation, VLAN tagging, MSI-X, Jumbo frames, IEEE 1588, and virtualization features such as VMware NetQueue and Microsoft VMQ. |  |
| Expansion Slots | Server should support minimum 9 PCI express 3.0 slots. |  |
| Storage Controllers | Should support 12Gbps SAS Controller with 4GB Flash Backed Write Cache. Controller should support data encryption to protect sensitive and mission critical data. Controller should support RAID levels 6, 60, 5, 50, 1, 10 and Advanced Data Mirroring with 3 drives |  |
| Storage Bays | Should be supplied with minimum Should support at least ten SFF HDDs |  |
| Hard Disk Drive | 5 x 1.2TB 12G SAS 10K rpm SFF (2.5-inch) Enterprise Hot pluggable Hard Drive and should be configured in RAID 6 with online spare HDD |  |
| Interfaces | System should support minimum of, Serial port: 1 Video: 1 front; 1 rear micro-SD Slot: 1 USB 2.0 Ports: 8 total: 2 front; 4 rear; 2 internal |  |
| Industry standard compliance | ACPI 2.0. Compliant PCIE 2.0 Compliant PXE Support WOL Support Physical Address Extension (PAE) Support Microsoft® Logo certifications USB 2.0 Support Ashrae A3/A4 |  |
| Power supply | Should support platinum efficiency hot plug redundant power supplies |  |
| (1) | (2) | (3) |
| System fans | Should support hot plug redundant system fans |  |
| Form Factor | 4 U Rack Mountable |  |
| Remote Management | 1. System remote management should support browser based Graphical Remote Console; Virtual Power button, Remote boot using USB / CD/ DVD Drive and should be capable to offer upgrade of software and patches from a remote client using Media / image/folder; server power capping and historical reporting; should have support for multifactor authentication. 2. Remote management port should be able to download the firmware from the website directly or from internal system. Server should support automated firware update. 3. Server should support agentless management using the out-of-band remote management port instead of OS and SNMP port on the OS. This will enable zero downtime updates 4. The server should support features which monitors and records changes in the server hardware and system configuration. It assists in diagnosing problems and delivering rapid resolution when system failures occur. 5. Remote console sharing with multiple users simultaneously during pre-OS and OS runtime operation, Console replay - Console Replay captures and stores for replay the console video during a server's last major fault or boot sequence. Microsoft Terminal Services Integration, 128 bit SSL encryption and Secure Shell Version 2 support. Should provide support for AES and 3DES on browser. Should provide remote firmware update functionality. Should provide support for Java free graphical remote console. |  |
| Server Management | System should provide support both UEFI and legacy system BIOS |  |
|  | The Systems Management software should provide Role-based security |  |
|  | Should help provide proactive notification of actual or impending component failure alerts on critical components like CPU, Memory and HDD. Should support automatic event handling that allows configuring policies to notify failures via e-mail, pager, or SMS gateway or automatic execution of scripts. |  |
|  | Server should support cloud based management by accessing the servers' configuration information, warranty & sla information, support case details anywhere from the internet |  |
|  | Should support scheduled execution of OS commands, batch files, scripts, and command line apps on remote nodes |  |
|  | Should be able to perform comprehensive system data collection and enable users to quickly produce detailed inventory reports for managed devices. Should support the reports to be saved in HTML, CSV or XML format. |  |
|  | Should help to proactively identify out-of-date BIOS, drivers, and Server Management agents and enable the remote update of system software/firmware components. |  |
| Warranty | Server Warranty includes 5-Year Parts, 5-Year Labor, 5-Year Onsite support with next business day response from OEM and vendor has to provide the letter from OEM |  |

- High end Server

- Category-2 	Quantity - 02 Nos.

| Parameters (1) | Specification (2) | A/D/N/C (3) |
| --- | --- | --- |
| Server: | Two CPU server with 14 core CPU |  |
| Item | Description of Requirement |  |
| CPU | Two No's of Intel® Xeon® E5-2660v4 (2.0GHz/14-core/35MB/105W) Processor Kit |  |
| CPU L3 CACHE Memory | 35 MB L3 cache |  |
| Motherboard | Intel® C610 Series Chipset |  |
| Memory | 128 GB DDR4 2400 MHz scalable to at least upto 768GB, using DDR4 Registered DIMM (RDIMM) memory modules with 24 DIMM slots or equivalent |  |
| Memory Protection | Advanced ECC with multi-bit error protection and memory online spare mode |  |
| HDD Bays | Up to 8 SFF, HDD/SSD expandable upto 16 drives with optional drive cage, The drive carrier should have intutive icon based display along with "DO NOT REMOVE" caution indicator that gets activated automatically in order to avoid data loss/downtime due to wrong drive removal or equivalent |  |
| Optical drive Bay | DVD-RW |  |
| Hard disk drive | 5 x 1.2TB 12G SAS 10K rpm SFF (2.5-inch) Enterprise Hot pluggable Hard Drive and should be configured in RAID 6 with online spare HDD |  |
| Controller | PCIe 3.0 based 12Gb/s SAS Raid Controller with RAID 0/1/1+0/5/50/6/60/1 Advanced Data Mirroring/10 Advanced Data Mirroring with 2GB battery backed write cache (onboard or in a PCI Express slot) |  |
| Networking features | 1Gb 4-port network adaptor supporting advanced features such as Large Send offload capability, TCP checksum and segmentation, VLAN tagging, MSI-X, Jumbo frames, IEEE 1588, and virtualization features such as VMware NetQueue and Microsoft VMQ. |  |
| Interfaces | Serial - 1 Micro SD slot - 1 USB 3.0 support With Up to 5 total: 1 front, 2 rear, 2 internal (secure) |  |
| Bus Slots | Six PCI-Express 3.0 slots, atleast two x16 and four x8 slots |  |
| Power Supply | Minimum 94%effecient Hot pluggable Redundant Power Supplies |  |
| Fans | Redundant hot-plug system fans |  |
| Graphics | Integrated video with 16MB of Video RAM |  |
| Industry Standard Compliance | ACPI 2.0b Compliant PCIe 3.0 Compliant PXE Support WOL Support Microsoft® Logo certifications USB 3.0 Support USB 2.0 Support Energy Star ASHRAE A3/A4 UEFI (Unified Extensible Firmware Interface Forum) |  |
| (1) | (2) | (3) |
| Embedded system management | Should support monitoring ongoing management, service alerting, reporting and remote management with embedded Gigabit out of band management port Server should support configuring and booting securely with industry standard Unified Extensible Firmware System should support RESTful API integration System management should support provisioning servers by discovering and deploying 1 to few servers with Intelligent Provisioning System should support embedded remote support to transmit hardware events directly to OEM or an authorized partner for automated phone home support |  |
| Security | Power-on password Serial interface control Administrator's password UEFI Should support upto 12 customizable user accounts on out of band management port and SSL encryption Should also supports directory services integration TPM 1.2 |  |
| Operating Systems and Virtualization Software Support | Microsoft Windows Server Canonical Ubuntu Red Hat Enterprise Linux (RHEL) SUSE Linux Enterprise Server (SLES) Oracle Solaris VMware Citrix XenServer |  |
| Provisioning | Essential tools, drivers, agents to setup, deploy and maintain the server should be embedded inside the server. There should be a built -in Update manager that can update firmware of system by connecting online. |  |
| Remote Management | 1. System remote management should support browser based graphical remote console along with Virtual Power button, remote boot using USB/CD/DVD Drive. It should be capable of offering upgrade of software and patches from a remote client using Media/image/folder; It should support server power capping and historical reporting and should have support for multifactor authentication. 2. Server should have dedicated 1Gbps remote management port. Remote management port should have 4GB NAND flash with 1GB available for user access. NAND flash should be used for keeping system logs and downloading firmware from website or internal repository 3. Server should support agentless management using the out-of-band remote management port. 4. The server should support monitoring and recording changes in the server hardware and system configuration. It assists in diagnosing problems and delivering rapid resolution when system failures occur. 5. Remote console sharing upto 6 users simultaneously during pre-OS and OS runtime operation, Console replay - Console Replay captures and stores for replay the console video during a server's last major fault or boot sequence. Microsoft Terminal Services Integration, 128 bit SSL encryption and Secure Shell Version 2 support. Should provide support for AES and 3DES on browser. Should provide remote firmware update functionality. Should provide support for Java free graphical remote console. |  |
| (1) | (2) | (3) |
| Server Management | The systems management software should provide Role-based security. |  |
|  | Should help provide proactive notification of actual or impending component failure alerts on critical components like CPU, Memory and HDD. Should support automatic event handling that allows configuring policies to notify failures via e-mail, pager, or SMS gateway or automatic execution of scripts. |  |
|  | Should provide an online portal that can be accesible from anywhere. The portal should provide one stop, online access to the product, support information and provide information to track warranties, support contrats and status. The Portal should also provide a Personalised daskboard to monitor device heath, hardware events, contract and warranty status. Should provide a visual status of individual devices and device groups. The Portal should be accessible on premise (at customer location - console based) or off premise (using internet). |  |
|  | Should support scheduled execution of OS commands, batch files, scripts, and command line apps on remote nodes |  |
|  | Should be able to perform comprehensive system data collection and enable users to quickly produce detailed inventory reports for managed devices. Should support the reports to be saved in HTML, CSV or XML format. |  |
|  | Should help to proactively identify out-of-date BIOS, drivers, and Server Management agents and enable the remote update of system software/firmware components. |  |
|  | The Server Management Software should be of the same brand as of the server supplier. |  |
|  | Infra Platform /Infra Software to support a variety of different hypervisors, such as VMware, Microsoft Hyper-V, Red Hat KVM |  |
|  | Solution available to Deploy a fast and easy installation via software appliance delivery mode. With its own OS and Database to provide infra and lifecycle management |  |
| Chassis | 2 U Rack Mountable |  |
| Warranty | Server Warranty includes 5-Year Parts, 5-Year Labor, 5-Year Onsite support with next business day response from OEM and vendor has to provide the letter from OEM |  |

iii) Low-End Servers: Quantity -24  Nos.

| Parameters (1) | Specification (2) | A/D/N/C (3) |
| --- | --- | --- |
| CPU | Intel® Xeon® E3-1220v5 (3.0GHz/4-core/8MB/80W) Processor Kit | 3 |
| CPU L3 CACHE Memory | 8MB (1x8MB) Level 3 |  |
| Motherboard | Intel® C236 Chipset |  |
| Memory | 8GB (1x8GB) DDR4-2133 scalable to 64 GB operating at 2133 MHz. |  |
| Memory Protection | ECC |  |
| Hard Disk Drive | 500GB 6G SATA 7.2K rpm SFF (2.5-inch) Hard Drive |  |
| HDD Bays | Minimum 8 SFF Hot plug Drive Bay |  |
| Optical drive | SATA DVD-RW Optical Drive |  |
| 1 |  |  |
| HDD carrier | Hard disk drive should support "Do Not Remove" caution indicator to avoid human errors in replacing failed HDD |  |
| Controller | RAID controller supporting RAID 0,1 and 5 |  |
| Networking features | 1Gb 2-port network adaptor |  |
| Ports | Minimum 6 USB 3.0 Ports Network RJ-45 (Ethernet):2 ; one video and one internal MICRO SD slot or equivalent or higher |  |
| Bus Slots | 4 PCI-3.0 Express slots with one x16 slot |  |
| Industry Standard Compliance | ACPI 2.0b Compliant |  |
|  | PCIe 3.0 Compliant |  |
|  | PXE Support |  |
|  | WOL Support |  |
|  | Microsoft® Logo certifications USB 2.0/3.0 Support |  |
| Security | Power-on password |  |
|  | Administrator's password |  |
|  | Server should also support Trusted Platform Module microcontroller chip that can securely store artifacts used to authenticate the server platform. These artifacts can include passwords, certificates and encryption keys. |  |
| OS Support | Microsoft Windows Server |  |
|  | Red Hat Enterprise Linux (RHEL) |  |
|  | SUSE Linux Enterprise Server (SLES) |  |
|  | VMware |  |
| Power Supply | Suitable power supply |  |
| Fans | Non-redundant Fan |  |
| Provisioning | Essential tools, drivers, agents to setup, deploy and maintain the server should be embedded inside the server. There should be a built -in Update manager that can update firmware of system by connecting online. |  |
| Remote Management | 1. System remote management should support browser based graphical remote console along with Virtual Power button, remote boot using USB/CD/DVD Drive. It should be capable of offering upgrade of software and patches from a remote client using Media/image/folder; It should support server power capping and historical reporting and should have support for multifactor authentication. |  |
|  | 2. Server should support agent less management using the out-of-band remote management port.. |  |
| Server Management | The Systems Management software should provide Role-based security |  |
|  | Should help provide proactive notification of actual or impending component failure alerts on critical components like CPU, Memory and HDD. Should support automatic event handling that allows configuring policies to notify failures via e-mail, pager, or SMS gateway or automatic execution of scripts. |  |
| Warranty | Server Warranty includes 5-Year Parts, 5-Year Labor, 5-Year Onsite support with next business day response from OEM and vendor has to provide the letter from OEM |  |
| Chassis | Tower |  |
| Monitor | 18.5 LED Monitor |  |
| Keyboard and Mouse | Keyboard and Mouse |  |

IV )  24 Port Switch (Network Switch): Quantity -30  Nos.

| Standards: | IEEE802.3,IEEE802.3u, and IEEE802.3ab standards |  |
| --- | --- | --- |
| Ports x speed: | 24 x RJ-45 10/100/1000Mbps |  |
| Support: | 24X 7 X365 days support. |  |
| Warranty: | 5 Years on site warranty. |  |
| Minimum System Requirements: | Connected devices need Ethernet connectivity and Ethernet cables |  |
| Package Contents: | Rack mountable 24-Port Gigabit Ethernet Switch along with required accessories |  |
| Specifications | Device Type : Switch - 24 ports Enclosure Type : Desktop/rack mountable Ports: 24 x 10/100/1000 + 2 x SFP Features : MDI/MDI-X switch, Auto-negotiation Compliant Standards: IEEE 802.3x, IEEE 802.3ab, IEEE 802.3u, IEEE 802.3 Status Indicators: Link activity, System |  |
| Expansion / Connectivity | Interfaces 24 x Ethernet 10Base-T/100Base-TX/1000Base-T - RJ-45; Expansion Slot(s) 2 (total) / 2 (free) SFP |  |
| Power Device | Internal Power supply |  |
| Environmental Parameters | Device should work under any Indian temperatures. |  |
| Warranty | Switch Warranty includes 5-Year Parts, 5-Year Labor, 5-Year Onsite support with next business day response from OEM and the vendor has to provide the letter from OEM |  |
| Make & Model | CISCO or Equivalent. |  |

V) Storage Device (NAS Drives “Back up Device”):  Quantity-  03 Nos.

| Parameters (1) | Specification (2) | A/D/N/C (3) |
| --- | --- | --- |
| HDD | 8-Bay or higher with 16 TB usable disk space |  |
| Memory | 16 Gb |  |
| Processor | Intel Xeon E5-2600 series or higher. |  |
| BIOS | BIOS should be of the same OEM |  |
| Network Interface | 2x1GbE (SFP+) Network, |  |